*Dryer tip!

Do you use dryer sheets in your dryer?  If so you should perform this test:

- clean all the lint from dryer filter

- run the filter under a faucet tap

If water runs right through it your filter is fine, if water stands and takes a bit to run through you have a plugged lint filter.  Do the following to unplug your filter:

- With warm soap water and a soft brush – old tooth brush works great, gently clean your dryer filter.

- Rinse thoroughly.

Water should run through with no problem of pooling on filter.  If there is still pooling repeat process. If you can not get the lint filter clean you should replace it. Why?  A plugged lint filter will/could burn out your dryers heating element and or heating sensors and limits.

Now before returning the lint filter to its place in your dryer be certain that it has dried thoroughly.

Further recommendations:

Have your dryer professionally cleaned by a trained service technician every 3-5 years depending on your usage and NEVER run your dryer without a lint filter in it.

*NOTE: any of our helpful hints that you try on your own are at your own risk.  Dale’s Refrigeration & Heating is not responsible for any things you try, you are assuming total responsibility!